## Slide 1
Technologie verrijkt de vakman
Vakman verrijkt de technologie
6 september 2022
Mark Peters
IJssel Technologie
Gerrit Ekelmans
IJssel Technologie

## Slide 2: IJssel Technologie
Opdracht: Productiebedrijven concurrerend maken
Organisatie: 450 medewerkers, 6 vestigingen
monteurs, engineers, bedrijfskundigen
Markt: Maak-, Food- & Proces Industrie
Diensten: Realiseren, onderhouden en verbeteren slimme fabrieken
Unieke combinatie: Nieuwe Technologie/Vakmanschap/Bedrijfskunde
Notes: 1 min:
I work for IJssel Technology
One of the Front runners in Smart Industry / Industry 4.0
in the Netherlands
Some of our key areas for innovation are: Next 3 sheets
3 min:
-bullets on this sheet

## Slide 3: SMARTPRODUCTION Making customer specific (n=1) production the new standard
Takt
05:04
Notes: Auping
Van productie op voorraad naar productie op order
Variatie spiralen: (Criade/Original 6b x 4l x 5t + Royal 3bx3lx5tx3kl ca. 300 types
Doorlooptijd staal van 1 week naar 3,5 uur
Voorraden van Van 12 mljn naar 3 mljn
Van Vuuren in Grou
Speciaaldeuren Utiliteitsbouw (specifieke eis deuren brandwerend/straling/geluid…)
Project ontwerp en realisatie geautomatiseerde paneelopbouwlijn
Klantspecifiek, met veel variatie (Vulling 6 varianten/randhout 8/dekplaat 6/HPL zichtlaag 100, laagvolgorde, afmetingen hoogte 300 – 3050 mm, breedte 300-1525)
Korte levertijden
Takt 25 seconden (1000 deuren per ploeg in dagdienst)
Projectwaarde ca. 7 miljoen (IJssel urendeel ca. 2 miljoen)
PJL Taco Overvliet, BK Clint Swager, Johan van Elven
Engineering Johan vd Kooij, Jan Rigterink, Wiebe Koning, Ko van Oldenbarneveld, Paul de Jong
IA Bauke vd Berg/Monique Akkerman, Tim van Dalfsen, IA bekabeling: Jan Kleefstra

## Slide 4: SMARTMAINTENANCE Leading industry towards zero (unplanned) downtime
Notes: 1 min:
Condition Based Predictive Maintenance
3 min:
We have developed a system called UptimeWorks
  Based upon highly accurate 24-bit vibration measurements
  is able to detect problems 2-3 months ahead
  so they can be solved during regular planned maintenance stops instead of leading towards unplanned downtime
Sytems operational at Tata Steel, Scania, Cargill and Coca Cola
Wireless Smart Sensors/Cloud-connectivity/Predictive Maintenance Algorithms
Extra:
Maintenance Algorithms
  Recognize and set alarms (anomaly detection)
  Automate Labeling problems (soft foot, alignment, inner/outer race/In-balance/Cavity)
  Predict remaining run-time before failure

## Slide 5: SMARTPEOPLE Realizing breakthrough performance improvements with people

## Slide 6: Uitdagingen in de industrie
Markt vraagt om
disruptief
betere prestaties
RELIABILITY
EFFICIENCY
QUALITY
SAFETY
SPEED
&
FLEXIBILITY
&
VARIETY
&
SUSTAINABILITY
&
Kansen door nieuwe techniek
Vergrijzing én beperkte instroom:
schaarste in vakmanschap
Slimme bedrijven
overleven
keer op keer
Techniek
Vakmanschap
Bedrijfskunde
Hogere beschikbaarheid
tegen lagere kosten
Managed assets
per professional
Uitdagingen in onderhoud

## Slide 7: Verrijken vakman in het veld
Notes: Under construction. Projectleider makkelijker toegang tot zijn projecten. inloggen citrix, acto (efficiëntie verbetering/project bewaking)
Urenapp: Harry van Zuthem
Ultimo Go: Tegenwoordig op alle plekken waar we overgaan op een nieuw onderhoudsbeheerssysteem gelijk de tablet/smartphone functionaliteit meegenomen
Mafuta: Aansturing van smeertechnisch onderhoud en visuele inspecties vanuit een internetdatabase naar de smartphone met mogelijkheid uitvoeringsfeedback rechtstreeks up te loaden (foto’s meetgegevenens, en opmerkingen)

## Slide 8: Verrijken vakman in de cloud
Smart sensors
WWW
Connectivity
Artificial Intelligence
Digitization
Industry 4.0
Cyber Physical Systems
Smart
Industry

## Slide 9: P-F Curve
MI
MI
uClip
MI
uBlock
Visual inspection Lubrication & IR
uBridge
Measurement Interval
(MI)
Failure starts
to occur
Early
Signal 1
Early
Signal 2
Early
Signal 3
Audible Noise
Hot to Touch
Detectable with:
24 bit
Point P
Desired performance level
Equipment
Failure
Detectable with:
Infra Red
Repair costs
Detectable
with:
16 bit
(Most of) Comparable
Alternative measurement systems

## Slide 10: Gestandaardiseerd meten
Standardized vibration measurements:
    RMS g
    ISO /Velocity
    Magnitude
    Crest factor
    Kurtosis
Standard addable measurements:
    RPM
    Temperature
    Current
    Oil quality
    Integration with other process data

## Slide 11: Conditie data analyseren in de cloud

## Slide 12: Integrated Condition Monitoring
Oil analysis
Lubrication
management
Mobile visual inspections and infra red
On-line & route based condition monitoring
Advise and Prediction
Expert
Analysis
Root Cause Analysis
Additional sensoring and process data
Ai
3. Dashboarding
2. Expert analysis & advise
Repair
Modify
Maint. Concept
1. Trend and Alarm reporting
Value reporting
Maintenance
Management
System
Api

## Slide 13: Live demo

## Slide 14: Vakman verrijkt nieuwe technologie

## Slide 15: AI en de vakman
Collecting Measurements
Detecting Anomalies/Alarms
Analyzing the Selection
Reporting findings
Improvement process

## Slide 16: AI en de vakman
Collecting Measurements
Detecting Anomalies/Alarms
Analyzing the Selection
Reporting findings
Improvement process

## Slide 17: AI en de vakman
Collecting Measurements
Detecting Anomalies/Alarms
Analyzing the Selection
Reporting findings
Improvement process

## Slide 18: AI en de vakman
Collecting Measurements
Detecting Anomalies/Alarms
Analyzing the Selection
Reporting findings
Improvement process

## Slide 19: AI en de vakman
Collecting Measurements
Detecting Anomalies/Alarms
Analyzing the Selection
Reporting findings
Improvement process