## Slide 1: AIRTUB WP 6: erosion MODELLING AND repair recipes
G. Schepers (TNO Energy Transition/ Hanze UAS)
WP 6: Erosion modelling and repair recipe

## Slide 2: WP6: Erosion Modelling and repair recipes
Participants:
TNO Energy Transition
Hanze UAS
HZ UAS
NLR
WP 6: Erosion modelling and repair recipe

## Slide 3: AIRTUB WP6: Goal
To answer the question: “How can we model the aerodynamic loss from a given blade erosion and the resulting loss in wind turbine energy production?”
To classify an arbitrary blade erosion into different categories
To develop a repair strategy for different erosion classes and implement it into a decision tool
From MLW Veraart Deterioration in aerodynamic performance due to leading edge rain erosion LM, DTU, TUDelft report 2017

## Slide 4: AIRTUB WP6: sUB Work Packages/Presentations
WP 6.1 Aerodynamics (Presented by kISHORE vimalakanthAN)
WP 6.2 Classification of erosion (Presented by Loek van der LINDE)
Guest presentation: Beatriz Mendez Lopez, Erosion activities at CENEr

## Slide 5: Procedure to determine energy loss from Erosion
  Input: lift and drag coefficient cl cd of each element with given airfoil shape as function of angle of attack a.
  Determine reduction in cl and increase in cd from erosion with:
              Lower fidelity engineering approach RFOIL (2D) with generalised erosion
              Higher fidelity CFD approach (2D) with generalised erosion (Kishore)
              Higher fidelity CFD approach with actual scanned 3D blade geometry (Kishore)
BASED ON: BLADE ELEMENT MOMENTUM THEORY (BEM)
36 %
18 %
c
dr
r

## Slide 6: Procedure to determine energy loss from erosion Procedure based on RFOIL
  Extension of approach from Sandia Laboratory (based on the publicly available XFOIL code and 1 set of wind tunnel measurements)
    Now: RFOIL and more measurements (2 airfoils, 4 Reynolds numbers, measurements performed by Sandia)
  Approach and assumptions :
    Aerodynamic effects erosion determined by forward shift of boundary layer transition point
    Forward shift is calculated from calibration curve f(Ik) Ik (height and density of roughness elements)
    f = 1: No shift; f < 1 Forward shift
    Calibrated with wind tunnel measurements
F(Ik) calibrated with wind tunnel measurements

## Slide 7: Laminar and turbulent flow

## Slide 8: Some results
Absolute difference between RFOIL approach and Sandia wind tunnel measurements, Different calibration curves cl, cd, and transition points as f(a) NACA63418 airfoil, Reynolds number 2.4e6.
Roughness relative height, k/c is 123 10 -6 Roughness density, d, is 15%.
Procedure to determine energy loss from erosion RESULTS FROM Procedure based on RFOIL

## Slide 9: Wind TUNNEL MEASUREMENTS ON cLEAN And ROUGH Airfoils
  NLR LST wind tunnel
  DU 00-W-212 airfoil (extensively measured in EU AVATAR project for clean conditions)
  Grained airfoils instead of sand paper
  Clean results differ from the known clean performance measured in AVATAR
  Possibly due to some (limited) 3D shape deviations
  Still some lessons from the experiment could be useful in follow-up experiments

## Slide 10: What about HIGH Reynolds numbers?
    Reynolds number (Re) is an aerodynamic scaling parameter, determined by size, velocity and viscosity
    Boundary layer transition depends heavily on Re
      Erosion effects largely determined by transition
    Off-shore wind turbines Re > 10 M
    (Conventional) Wind tunnel measurements Re < 6M
    Within the EU project AVATAR measurements on clean airfoils have been done in a pressurized wind tunnel up to Re =15 M.
      XFOIL (RFOIL) can predict airfoil performance at RE = 15 M well; CFD predicts airfoil performance at Re = 15 M poorly
      Explanation: boundary layer transition model: eN (XFOIL/RFOIL), SSTLM (CFD)
    SSTLM makes use of a calibration curve between turbulence intensity and transition onset momentum thickness Reynolds number Req,t
    SSTLM relation needs adjustment or SSTLM model itself needs adjustment for higher Re
      M. Caboni Validation of high Reynolds number, free-transition, RANS-based CFD simulations using the DNW-HDG's airfoil experiment, TNO 2021 R12123 , Public report, December 2021

## Slide 11: conclusions frOM This presentaton
  RFOIL can be used to determine the aerodynamic losses from erosion in an efficient public domain approach
    Determination of a generalised Ik from erosion patterns may need some experience
    Calibrate f(Ik) for a situation as representative as possible
    OR….
    Use CFD from generalised erosion or from the actual deformed blade (Kishore)
  More research is needed for erosion effects at high Reynolds numbers
  More information in [1] [1] .G. Schepers, N. Adema, M. Caboni, K. Vimalakanthan, M.J. Vermeulen WP6.1 Aerodynamic modelling of wind turbine blades exposed to erosion, TNO report, available in draft

## Slide 12: WP 6.1 DELIVERABLES
      M. Caboni Validation of high Reynolds number, free-transition, RANS-based CFD simulations using the DNW-HDG's airfoil experiment, TNO 2021 R12123 , Public report, December 2021
      K. Vimalakanthan CFD transition model for rough surfaces TNO 2021 R12579, Public report, December 2021
      K. Vimalakanthan Aerodynamic performance prediction of eroded and rough wind turbine blade sections using RANS CFD. EERA workshop on blade erosion from the perspective of loads, controls and aerodynamics, December 14, 2022 SP4 WORKSHOP on Blade Erosion from the prospective of loads, controls and aerodynamics | EERA JP Wind
      I. Lallelis Model Validation for Simulating the Effects of Leading Edge Erosion Hanze/TNO Student thesis report, January 2019.
      O. Shamir: Analysis of LM wind tunnel measurements at erosion. Public Hanze report, November 2020
      J. Nwaehie: Automation of IRPWIND roughness experiment, InHolland/TNO Student thesis report September 2020
      M.J. Vermeulen: Erosion on wind turbine blade wind tunnel test, NLR-CR-2021-516, September 2021
      Kisorthman Vimalakanthan, Harald van der Mijle Meijer, Iana Bakhmet, and Gerard Schepers Performance modeling of eroded wind turbine blade using CFD, Preprint for Journal of Wind Energy Science https://wes.copernicus.org/preprints/wes-2022-65/
      J.G. Schepers et al: Summary of Airtub WP6.1 results, Available in draft, in review at project partners

## Slide 13: Acknowledgements
  TKI WOZ For Funding Airtub project
  Sandia Laboratory (D. Maniaci) for wind tunnel measurements
  Zephyros: Ferry Visser, Jeroen Verschelling for coordination